## Slide 1: draft-eckert-anima-grasp-dnssd-00
IETF’100 Singapore, November 2017
DNSSD WG, version 2
Toerless Eckert, Huawei (Futurewei Technologies USA)
tte+ietf@cs.fau.de

## Slide 2: ANIMA WG solution
ANI/ACP: Autonomic - Network Infrastructure / Autonomic Control Plane
  Automatically built, hop-by-hop encrypted VRF (VRF-lite) – to manage/control networks:
    Autonomic: between autonomic software in network
      Management/service agents, distributed protocol instances, …
    Classical/SDN: network-devices <-> NOC (NMS/controller/orchestrator/provisioning)
ACP/ANI: Only IPv6 unicast routing/forwarding
  No definition/requirement for DNS names – AND NO IP multicast
GRASP: protocol for discovery, synchronization, negotiation
  Discovery: Announcement and Request messages: (M_FLOOD, M_DISCOVERY)
    Network wide hop-by-hop reliable flooded across ANI/ACP
  Header: objective-name (string), hop-count, sequence number (loop-prevention)
    objective-name” is the “address” for logical endpoints sending/receiving flooded GRASP messages..
  Payload: undefined – up to each application (per “objective”)
    Encoding mandatory though: CBOR (message header and payload)

## Slide 3: Use cases
Autonomic, required by ANI/ACP itself:
  Bootstrap servers (“BRSKI”).
    ANI network devices provide bootstrap helper functionality. Connect to bootstrap servers.
  Servers for renewal of keying material used to protect ANI/ACP (“EST” – RFC7030).
  … more in future
Traditional OAM model:
  Variety of services in NOC to be discovered by (all or many) network devices to auto-configure those services – and provide automatic server failover:
    Syslog
    Time (NTP)
    Netconf (call-home)
    DHCP server, DNS server
    Radius, Diameter, Tacacs (authentication servers)
    WiFi controller (for AP devices)
    IPfix, any other data collection export
    tftp (“yuck”)
    List goes on…

## Slide 4: OK, sounds great… why this draft again ?
Do not re-invent for ANI/ACP GRASP aspects of service discovery we already know (and love) from DNS-SD
  Page 1: Payload: undefined – up to each application (per “objective”)
    Not every flooded GRASP objective is a service (announce/request), but if it is, then reuse common definitions!
  But keep as simple as possible
    Do not inherit historic crud (e.g.: _udp, _tcp)
    Difference in functionality to unicast DNS – GRASP flooding more like mDNS and .local
So, what do we have with DNS-SD ?
  Service name space – RFC6335 (e.g.: “brski”, “est”, …)
  Service selection criteria (prio, weight)
  Service instance names (for browsing… how useful without human selection)
  “Host-names” of service instances – not needed ?!
  … (draft-00 has hopfully mapped the 90% important parameters)

## Slide 5: DNS-SD compatible GRASP objectives (CDDL):
objective-name //= SRV.<rfc6335-service-name>
objective-name //= NAME.<hostname> ….......... If we ever need them
service-element = {
?( &(private:0) => any), ............. Non-standardized extensions
?( &(msg-type:1 => msg-type
?( &(service:2) => tstr),............. Service Name (“printer“)
*( &(instance:3) => tstr),............. Instance Name („my-kitchen-printer“)
?( &(domain:4) => tstr),............. Empty = ANI/ACP (like .local), else VRF name
?( &(priority:5) => 0..65535 ),........ As in DNS-SD
?( &(weight:6) => 0..65535 ),........ As in DNS-SD
*( &(kvpairs:7) => { *(tstr: any) },.. Key Value pairs – as in DNS-SD
?( &(range:8) => 0..255 ),.......... For distance based service selection
*( &(clocator:9) => clocator),......... GRASP locators with context indicator (“VRF”)
}
clocator = [ context, locator-option ] ......... Permit locators to be in data plane
context = tstr ................................. Empty: ACP, „0“ = „VRF0“, else name of VRF
locator-option = <unchanged> ................... from GRASP specification – IPv4/IPv6addr/port
msg-type = &( describe: 0, describe-request:1, enumerate:2, enumerate-request:3 ).

## Slide 6: Target system
Simpler, more consistent specification of ANI/ACP services:
  “service has <name> in IANA registry, parameters according to DNSSD/GRASP” - DONE
Common service announce/discover API/SDK for servers/clients:
  Could map to DNS-SD and/or GRASP based on context
mDNS <-> GRASP services gateway function in NOC router
  NOC servers could use mDNS (more and more supported already, free SDKs, proven)
  gateway converts to GRASP,
  ANI/ACP clients use GRASP
Outside ANIMA scope:
  Gateway function for any service announce/discovery of non-OAM services
    Produced consumed directly by non-network infra (clients)
  Not limitation of technology but of ANIMA goals:
    GRASP flooding (with ANI or modified underlying transport) could be alternative to draft-ietf-dnssd-hybrid
    Technically: Flooding in GRASP makes solution more applicable to services with dense client distribution (everybody needs to know about these services).

## Slide 7: References / details
Presentation of DNS-SD draft in ANIMA on Monday
draft-ietf-anima-grasp
draft-ietf-anima-autonomic-control-plane (ACP)
draft-ietf-anima-bootstrap-keyinfra (BRSKI)
draft-ietf-anima-stable-connectivity (NOC services framework)